A baseline inventory of epilithic diatom diversity in lowland Irish rivers

Heritage Council Funded Project WLD/2002/59

# Final Report

# November 24 2002

T.J. Harrington and B. Ní Chatháin

Department of Life Sciences

University of Limerick

# Table of Contents

|  | Page |
| --- | --- |
| Summary | 3 |
| Introduction | 5 |
| Methods | 8 |
| Results | 9 |
| Species composition | 9 |
| Diatom occurrence and abundance | 11 |
| DCA analysis | 15 |
| Trophic Diatom Index | 20 |
| Discussion | 22 |
| Rfeferences | 25 |

# Summary

Algae form an important component of aquatic ecosystems and diatoms are probably the most widespread and abundant of all groups of benthic algae. Diatoms (Bacillariophyta) are unicellular and unique amongst photosynthetic organisms in having a rigid siliceous wall (frustule) around the cytoplasm. They are classified to species level primarily on the basis of symmetry and ornamentation of the frustule. In many European countries and North America, diatoms have been used successfully as indicators of eutrophication in rivers. Few studies have investigated the composition of epilithic diatom assemblages in Irish rivers (Foged 1977, Heuff and Horkan 1984, and Ní Chatháin 2002). This project aimed to address this deficiency by investigating the composition and distribution of epilithic diatom assemblages in lowland base-rich rivers in Ireland. Twenty-five lowland rivers were sampled in August and September 2002. Reference Naphrax® -mounted slide collections of diatoms were prepared from each of the rivers sampled.

Seventy-one diatom species were identified from the 25 lowland rivers sampled.  The number of species identified per river ranged between 17 and 32 and these numbers can be considered as generally high and also comparable with other studies in Ireland, Britain and Europe. All rivers were characterized by a small number of species that became abundant, and a large number of species that occurred occasionally or on one occasion only. This is a well-known characteristic of diatom assemblages and algal communities in general. Only 22 species (31%) were identified from ten or more rivers investigated, and only 16 species (22.5%) were identified from 15 or more rivers investigated. Several species occurred in a large number of the river samples and dominated these assemblages. These species include, Amphora pediculus, Achnanthes minutissima, Cocconeis placentula, Gomphonema minutum, Navicula tripunctata, and Rhoicosphenia abbreviata. The majority of the species identified were epilithic species. Some species however, are common on silt-covered stones, particularly in lowland streams (e.g. Navicula tripunctata and Navicula lanceolata), and some are epiphytic species, common on Cladophora glomerata filaments (e.g. Cocconeis placentula and Rhoicosphenia abbreviata).

Detrended correspondence analysis of diatom species distribution showed that there were discontinuities in distribution of even common diatom species between the rivers. A group of six rivers (Nenagh R., King’s R. (Kilkenny), Dinin,  Erkina, Anner and Multeen) were found to have diatom assemblages which differed significantly in composition to most of the other rivers sampled. Applying the Trophic Diatom Index (a measure of trophic status of the river based on diatom diversity) to the data indicated that all rivers showed some signs of nutrient enrichment and some (e.g. Boyne, Camlin, Erkina, Maigue, Mulcair) showed marked signs of  eutrophication.

Introduction

Diatoms (Fig. 4) are microalgae of marine and freshwater environments and comprise 285 genera (Round et al., 1990) with between 10000-12000 recognized species (Norton et al., 1996). They are abundant in freshwaters where they are among the most important aquatic photosynthesizers (Graham and Wilcox, 2000).  Diatoms have an extensive fossil record going back to the Cretaceous; some rocks are formed almost entirely of fossil diatoms, and are known as diatomite or diatomaceous earth.

Diatoms occur as single cells or chains of cells, and there are some filamentous forms.  In some species, the cells can be as large as 1 millimeter in diameter, although most are much smaller.  In lakes and seas, planktonic forms are predominant while in rivers, benthic forms predominate. There are two basic types of cell morphology: elongated forms called pennate diatoms which are most often found in freshwaters, and centric diatoms which are circular, triangular, or irregular in shape and are most abundant in the ocean.  The hemicellulose cell wall of a typical diatom is heavily impregnated of silica and is composed of two interlocking halves known as frustules, which fit together, one of top of the other, like the two parts of a pillbox.  Diatom frustules are generally highly ornamented, with variations in this ornamentation reflecting taxonomic diversity (Graham and Wilcox, 2000). The top of the frustule, the epitheca, is perforated with many holes, arranged in a pattern characteristic of the species.  The holes permit the cell's plasma membrane to maintain close contact with the environment, and allows for the diffusion of materials into and out of the cell. Numerous pores also reduce the weight of the floating diatom.  Some diatoms also have longitudinal slots in the wall of the base, or hypotheca, through which the cell can make contact with solid surfaces.  Such contact usually evokes a gliding ‘snail-like’ movement of unknown mechanism. This motility is regarded as a means by which diatoms may avoid local nutrient limitation and shading (Graham and Wilcox, 2000).  Diatoms contain chlorophyll a and c, and most have accessory xanthophylls such as fucoxanthin, which confer an olive-green to brownish colour on the cells.  Diatoms reproduce through cell division-one cell divides into two cells. After a diatom cell divides each new cell retains one frustule of the parent cell and builds a new frustule to fit into it.

Diversity and ecology of diatoms in Irish rivers

There is very little published information on the diversity of diatoms in Irish freshwaters and what exists mainly concerns diatoms in Irish lakes (e.g. Bowman 1985, Dalton 2002).  The only intensive study of river diatoms has been carried out on the R. Deel, Co. Limerick (Ní Chatháin, 2002).  In river systems, diatoms form extensive colonies on boulders and smaller stones (epilithic diatoms) and are grazed upon by freshwater invertebrates.  Individual diatom cells are attached to the rock surface by gelatinous stalks.  The greatest diversity of diatoms are found in unshaded, shallow, fast-flowing riffles with extensive areas of cobble-sized stones. Attached or benthic diatoms are also found in the interstices of sandy substrates (epipelic diatoms) and as epiphytes on aquatic macroalgae and macrophytes.  The composition and distribution of the diatom assemblages in a river are the result of environmental conditions within the river.  Diatom species have optima with respect to their tolerance (or preference) for environmental conditions such as nutrients, organic pollution, and pH among other factors, and polluted waters will tend to support an increased abundance of tolerant species (CEN 13946, 2000).  Conversely, certain species are intolerant of elevated levels of one or more pollutants, whilst others can occur in a wide range of water qualities.  Considerable interest has centered on diatoms because these responses may provide information on water quality

Diatom species are very sensitive to water quality, eutrophication and pollution, and their ecological tolerances are well documented in Europe (Whitton et al., 1991; Whitton and Rott, 1996; Prygiel et al., 1999).  The use of diatoms as indicators of water quality has been widespread in Europe, the U.S. and Japan over the past four decades (Sabater et al., 1987).  The lack of baseline information on diversity and distribution of diatoms in Irish rivers has meant that it has not been possible to use diatoms for water quality assessment in Ireland.  The information deficit needs to be addressed urgently for lowland rivers because eutrophication and other anthropogenic impacts are most severe in this category of rivers (Lucey et al. 1999).  The principal aim of this study is therefore, to survey the diversity of epilithic diatoms in a selection of Irish lowland rivers, the results of which will provide an essential cornerstone for future diatom-based assessments of river water quality in Ireland.

Project overview

This investigation focused on the diversity of epilithic diatoms only i.e. diatoms which grow on hard, relatively inert substrata such as pebbles, cobbles and boulders. This association has been focused on more often than not for use as part of water quality assessment purposes, and guidance standards for the routine sampling of benthic diatoms for the purposes of the Water Framework Directive (WFD, 2000) have recommended the use of cobbles, pebbles and boulders as the preferred substratum. This report provides results for the investigation of the diversity of the epilithic diatom assemblage in twenty-five Irish lowland rivers.

Methods

Sampling, pretreatment and enumeration of epilithic diatoms from cobble substrata

Benthic diatom samples were collected from cobble substrata (epilithic diatoms) in July, August and September 2002. A list of the sites sampled is given in Table 1.  The epilithic diatom assemblage was sampled following recommendations outlined in CEN (2000). Riffle areas within the selected sampling sites were the preferred source of cobble substrata. Cobbles selected were those free from sediments and if possible, from any filamentous algal growths, both of which greatly reduce the diversity of epilithic diatoms. Five cobble samples were collected per site. The epilithic diatom assemblage was then removed from a defined area of each cobble by brushing with a toothbrush. Samples were then pooled for each river. Each sample was digested with 30% H2O2 and potassium dichromate to remove organic matter by oxidation.

Table 1. List of rivers sampled, site locations and grid references.

| No. | River | Site | Grid Ref |
| --- | --- | --- | --- |
| 1 | Aherlow | Cappa Old. Br. | R 990 290 |
| 2 | Anner | Br. SW Kilusty Castle | S 250 330 |
| 3 | Ara | Bansha Br. | R 975 315 |
| 4 | Boyne upper | Inchamore Br. | N 715 500 |
| 5 | Camlin | Mullagh | N 120 760 |
| 6 | Canahowna | At old mill, Gort | M 450 020 |
| 7 | Clare | Tuam | M 410 500 |
| 8 | Dead | At Dromkeen | R 740 480 |
| 9 | Deel | At Raharney | N 600 530 |
| 10 | Dinin | Dinin Br. | S 480 640 |
| 11 | Erkina | Durrow | S 410 770 |
| 12 | Gweestion | Outside Bohola | M 340 970 |
| 13 | Kilcolgan | Kilcolgan | M 440 185 |
| 14 | Kilmastulla | Cool Br. | R 710 595 |
| 15 | Kings | Br. N of Stonyford | S 470 430 |
| 16 | Little Brosna | Shinrone | S 080 940 |
| 17 | Maigue | Br. Near Rosstemple station | R 540 370 |
| 18 | Mulkear | Annacoty Br. | R 640 570 |
| 19 | Multeen | Ballygriffin Br. | S 050 405 |
| 20 | Nenagh | Br. D/s Nenagh Br. | R 870 820 |
| 21 | Nore | Old Town | S 415 840 |
| 22 | Silver | Kilcormac | N 180 135 |
| 23 | Sinking | Miltown | M 415 635 |
| 24 | Suir | Golden Br. | S 010 385 |
| 25 | Tar | Br. U/s Tar Br. | S 110 140 |

The H2O2 was then decanted, and distilled water added, and the contents mixed thoroughly to remove any remaining H2O2. The samples were then centrifuged at 3000 rpm for five minutes and the supernatant decanted. This washing step was repeated five times. The final slurries were placed in labeled 50 ml vials. The slurries were pipetted onto 19 mm circular coverslips (thickness 0) in a series of dilutions per sample. These coverslips were then dried slowly on a warm hotplate and a preliminary check of the density of the diatom valves on the coverslips was made to ensure the sample were not too dense, too dilute, or still contained organic matter or partially digested diatom cell contents. The coverslips were mounted onto glass microscope slides using Naphrax® mounting medium (R.I.= 1.7, Northern Biological Supplies, England). Diatom valves were identified and counted in random fields of view at x 1000 using Nomarski optics until 200 valves per slide were enumerated and identified. A further scan of the slide was also made to ensure all species present were accounted for. Identifications of prepared diatoms were made primarily with the monographs of Krammer and Lange-Bertalot (1986-1991).

##### Physico-chemical water quality data

At each sampling site/river, temperature, dissolved oxygen, conductivity, total dissolved solids and depth readings were taken by the researcher. Additional physico-chemical data was then obtained from the County Council or EPA laboratory responsible for the individual rivers. This data included information on levels of orthophosphate, nitrates, ammonia, biological oxygen demand and pH.

## Results

### Species composition

Seventy-one epilithic diatom species were identified from twenty-five lowland Irish rivers sampled in August and September 2002. These species plus authorities are listed in Table 2. No species was common to all twenty-five rivers. Three species were common to twenty-four rivers (Multeen excluded) and they were Achnanthes minutissima (Fig. 4k), Amphora pediculus and Cocconeis placentula (Fig. 4b). Thirty-four percent (24 species) of all species identified were found on one occasion only. These species can be considered as rare in their occurrence. The number of species identified per river is listed in Table 3. An average of 23.5 species were identified per river. The highest number of species was recorded in the R. Tar, with thirty-two species identified. The lowest number of species was recorded in the R. Gweestion with seventeen species.

Table 2. Epilithic diatom species identified from twenty-five Irish lowland rivers.

Numbers refer to Fig 3.

| No. | Species name |
| --- | --- |
| 1 | Achnanthes biasolettiana Grunow |
| 2 | Achnanthes lanceolata (Brébisson) Grunow |
| 3 | Achnanthes minutissima Kützing |
| 4 | Achnanthes oblongella Oestrup |
| 5 | Achnanthes sp.1 |
| 6 | Amphora montana Krasske |
| 7 | Amphora pediculus (Kützing) Grunow |
| 8 | Aulacoseira ambigua (Grunow) Simonsen |
| 9 | Caloneis bacillum (Grunow) Cleve |
| 10 | Cocconeis placentula Ehrenberg |
| 11 | Cocconeis pediculus Ehrenberg |
| 12 | Cyclotella meneghiana Kützing |
| 13 | Cyclotella radiosa (Grunow) Lemmermann |
| 14 | Cymbella aspera (Ehrenberg) Cleve |
| 15 | Cymbella minuta Hilse |
| 16 | Cymbella silescia Bleisch |
| 17 | Cymatopleura solea (Brébisson) W. Smith |
| 18 19 | Denticula tenuis Kützing Diatoma ehrenbergii Kützing |
| 20 | Diatoma tenuis Agardh |
| 21 | Diatoma vulgaris Bory |
| 22 | Eunotia arcus Ehrenberg |
| 23 | Fragilaria capucina Desmazières |
| 24 | Fragilaria construens (Ehrenberg) Grunow |
| 25 | Fragilaria capucina var. perminuta (Grun.) Lange-Bertalot |
| 26 | Fragilaria capucina var. vaucheriae (Kützing) Lange-Bertalot |
| 27 | Frustulia rhoimboides (Ehrenberg) De Toni |
| 28 | Gomphonema angustum Agardh |
| 29 | Gomphonema minutum (Agardh) Agardh |
| 30 | Gomphonema olivaceum (Hornemann) Brébisson |
| 31 | Gomphonema parvulum Kützing |
| 32 | Gyrosigma acuminatum (Kützing) Rabenhorst |
| 33 | Melosira varians Agardh |
| 34 | Meridion circulare (Greville) Agardh |
| 35 | Navicula atomus (Kützing) Grunow |
| 36 | Navicula bacillum Ehrenberg |
| 37 | Navicula capitata Ehrenberg |
| 38 | Navicula capitatoradiata Germain |
| 39 | Navicula cari Ehrenberg |
| 40 | Navicula cryptocephala Kützing |
| 41 | Navicula cryptotenella Lange-Bertalot |
| 42 | Navicula gregaria Donkin |
| 43 | Navicula lanceolata (Agardh) Ehrenberg |
| 44 | Navicula menisculus Schumann |
| 45 | Navicula minuscula Grunow |
| 46 | Navicula schoenfeldii Hustedt |
| 47 | Navicula subminuscula Manguin |
| 48 | Navicula sp. small 1 |
| 49 | Navicula halophila (Grunow) Cleve |
| 50 | Navicula subhamulata Grunow |
| 51 52 | Navicula tripunctata (O.F. Müller) Bory Navicula veneta Kützing |
| 53 | Nedium dubium (Ehrenberg) Cleve |
| 54 | Nitzschia dissipata (Kützing) Grunow |
| 55 | Nitzschia fonticola Grunow |
| 56 | Nitzschia palea (Kützing) W. Smith |
| 57 | Nitzschia perminuta (Grunow) M. Peragallo |
| 58 | Nitzschia recta Hantzsch |
| 59 | Navicula sleisvicensis Grunow |
| 60 | Reimeria(Cymbella) sinuata Gregory |
| 61 | Rhoicosphenia abbreviata (Agardh) Lange-Bertalot |
| 62 | Amphora inariensis Krammer |
| 63 | Gomphonema affine Kützing |
| 64 | Unidentified 1 |
| 65 | Fragilaria sp.1 |
| 66 | Fragilaria sp.2 |
| 67 | Surirella sp. |
| 68 | Stauroneis phoenicenteron (Nitzsch) Ehrenberg |
| 69 | Surirella angusta Kützing |
| 70 | Surirella brebissonii Krammer & Lange-Bertalot |
| 71 | Synedra ulna Ehrenberg |

# Diatom occurrence and abundance

# Figure 1 shows the relationship between diatom occurrence and maximum abundance in the river samples. The majority of the species plotted in the lower left corner and occurred at low abundances in relatively few river samples. However, several species occurred in a large number of the river samples and dominated these assemblages. These species include Amphora pediculus, Achnanthes minutissima, Cocconeis placentula, Gomphonema minutum, Navicula tripunctata, and Rhoicosphenia abbreviata. Some species, although of frequent occurrence, were not very abundant in any sample e.g. Navicula cryptotenella, Navicula lanceolata and Synedra ulna (Fig. 4e). A larger group of less frequent species often reached high maximum abundances in individual rivers e.g. Cocconeis pediculus (Fig. 4c), Caloneis bacillum (Fig. 4f), Nitzschia palea, Navicula gregaria, Achnanthes lanceolata, Fragilaria capucina var. vaucheriae, Gomphonema olivaceum, Cymbella minuta, Synedra ulna and Nitzschia dissipata.  Only 40 species (56.3%) reached an abundance of greater than or equal to 1% abundance in the river samples. Only 22 species (31%) were identified from ten or more rivers investigated, and only 16 species (22.5%) were identified from 15 or more rivers investigated.

Table 3. Number of diatom species identified from each site.

| No. | River | Number of species identified |
| --- | --- | --- |
| 1 | Aherlow | 24 |
| 2 | Anner | 23 |
| 3 | Ara | 25 |
| 4 | Boyne upper | 24 |
| 5 | Camlin | 25 |
| 6 | Clare | 24 |
| 7 | Dead | 28 |
| 8 | Deel | 25 |
| 9 | Dinin | 22 |
| 10 | Erkina | 23 |
| 11 | Gort | 18 |
| 12 | Gweestion | 17 |
| 13 | Kilcolgan | 20 |
| 14 | Kilmastulla | 20 |
| 15 | Kings | 22 |
| 16 | Little Brosna | 27 |
| 17 | Maigue | 27 |
| 18 | Mulkear | 26 |
| 19 | Multeen | 27 |
| 20 | Nenagh | 21 |
| 21 | Nore | 22 |
| 22 | Silver | 19 |
| 23 | Sinking | 24 |
| 24 25 | Suir Tar | 24 32 |

# Species with few occurrences and at times only a single occurrence included species not listed in Fig. 1, e.g. Cymatopleura solea, Denticula tenue, Eunotia arcus, Nedium dubium, Surirella angusta and Navicula veneta amongst others. These species can be considered as rare. 24 species (33.8%) were found in one river only and are therefore considered as rare.

# Detrended correspondence analysis of diatom distribution

The distribution of diatom species between the sites was examined using detrended correspondence analysis (DCA). The DCA plot in Fig. 2 illustrates relationships between the rivers based on composition of the diatom assemblages. No count could be made for the Cannahowna River (Galway) due to the very sparse presence of diatoms. Two or more points that are close together on the DCA plot will have a similar floristic composition, with many species in common, whereas those far apart will share very few species. Any two points more than three standard deviation (axis) units apart will share no common species (Kent and Coker, 1992). Therefore, the Multeen can be considered as having a dissimilar species composition to that of the rivers Ara and Little Brosna. From Figure 2 the rivers sampled can clearly be seen to differ in their species composition, with for example the upper Boyne plotting to the top right of the plot, the Aherlow, Gweestion, Silver, Sinking, Clare, Camlin, and Dead plotting relatively close together near the top centre of the plot, while the Dinin, Kings, Nenagh, Erkina and Anner rivers all plotted to the bottom centre of the plot. The rivers Nore, Suir, Kilcolgan, Kilmastulla, Deel, Ara and Little Brosna also plotted relatively close together. The rivers Tar, Boyne upper and Multeen in particular have considerably different species compositions as illustrated by their plotting at the outer edges of Figure 2.

Figure 3 illustrates the diatom species plot for these river samples. Each species is illustrated by number (refer to Table 2 for species names). The majority of species can be seen to plot to the centre of the plot in the same position as the rivers Dead, Aherlow, Gweestion, Silver, Sinking, Clare, Camlin, Mulkear and Maigue plotted in Figure 2. This grouping included frequent species and those which also reached high abundance e.g. Achnanthes minutissima (3), Cocconeis placentula (10), Rhoicosphenia abbreviata (61), Navicula lanceolata (43), Navicula gregaria (42), Gomphonema minutum (29) and Nitzschia dissipata (54). In comparison the grouping of species to the bottom of Fig. 3 are more common to the rivers Dinin, Kings, Nenagh, Erkina and Anner and included Amphora pediculus (7), Fragilaria capucina var. vaucheriae (26), Reimeria sinuata (60) and Gomphonema angustum (28).

Application of the Trophic Diatom Index (TDI)

The Trophic Diatom Index is a measure of the of the trophic status of river water (predominately dissolved phosphorus concentration) based on the composition of the diatom assemblages (Kelly and Whitton, 1995). This index is computed using a “weighted average” equation and is calculated as follows:

TDI = (WMS x 25) -25

Where WMS = Weighted Mean Sensitivity, calculated as follows:

where aj = abundance (proportion) of taxon j in the sample, sj = pollution sensitivity (1-5) of taxon j, and vj = the indicator value (1-3) of species j.

Values of sensitivity are as follows: 1 = favoured by very low nutrient concentrations; 2 = favoured by low nutrient concentrations; 3 = favoured by intermediate concentrations of nutrients; 4 = favoured by high concentrations of nutrients, and 5 = favoured by very high concentrations of nutrients. The TDI is expressed on a scale from 0 to 100, 100 indicating a very eutrophic site. A second calculation is also included in the TDI and this is the calculation of the percent motile species, which is used as an indication of the reliability of the TDI. This calculation attempts to identify factors other than those related to water quality e.g. current speed, grazing, light availbility etc. that may be influencing the TDI score. The calculation of % motile species is recommended for making broad comparisons between samples which may highlight non-nutrient factors influencing the flora (Kelly et al., 2001). Results of the TDI and % motile species are presented in Table 4.

Table 4. Results from the calculation of the Trophic Diatom Index and % motile species.

| No. | River | TDI | % Motile species |
| --- | --- | --- | --- |
| 1 | Aherlow | 65.3 | 12.9 |
| 2 | Anner | 73.6 | 5.0 |
| 3 | Ara | 52.4 | 26.8 |
| 4 | Boyne upper | 73.6 | 18.7 |
| 5 | Camlin | 82.4 | 13.1 |
| 6 | Clare | 64.9 | 23.3 |
| 7 | Dead | 66.5 | 36.9 |
| 8 | Deel | 44.5 | 10.9 |
| 9 | Dinin | 56.3 | 3.4 |
| 10 | Erkina | 84.7 | 3.3 |
| 11 | Gweestion | 54.6 | 27.1 |
| 12 | Kilcolgan | 41.2 | 4.6 |
| 13 | Kilmastulla | 40.9 | 0.9 |
| 14 | Kings | 67.2 | 7.7 |
| 15 | Little Brosna | 51.9 | 8.1 |
| 16 | Maigue | 80.5 | 29.8 |
| 17 | Mulcair | 73.1 | 39.8 |
| 18 | Multeen | 67.0 | 51.0 |
| 19 | Nenagh | 50.6 | 4.5 |
| 20 | Nore | 48.3 | 21.7 |
| 21 | Silver | 50.7 | 11.2 |
| 22 | Sinking | 70.1 | 26.6 |
| 23 | Suir | 51.1 | 7.5 |
| 24 | Tar | 54.5 | 31.5 |

The TDI scores for the rivers Anner, Boyne upper, Camlin, Erkina, Maigue, Mulkear and Sinking indicate fairly eutrophic river sites. The species influencing the scores for these rivers differed, with the exception of Cocconeis placentula, which reached >10% abundance in all rivers. Amphora pediculus was particularly abundant in the Anner (44%) and the Erkina rivers (66%). Navicula tripunctata reached >10% in the Sinking, Boyne upper and the Camlin. All with the exception of the Mulkear also have reasonably low % motile species indicating that it was predominantly nutrient factors influencing the TDI score. The rivers Deel, Kilcolgan and Kilmastulla had the lowest TDI scores indicating sites of reasonably good quality.

Discussion

The river samples in general had high species diversity and were characterized by a small number of species that became abundant and a large number of species that occurred occasionally or on one occasion only. This pattern of abundance has also been documented in a number of diatom river studies (Van Dam 1982, Round 1993, Kelly et al. 1995, Allott and Flower 1997, Goldsmith 2000, and Ní Chatháin 2002), and the majority of papers report 1-5 species dominant at any one site. The number of species identified per river ranged between 17 and 32. This number is lower than the number of species per sample recorded from the R. Deel, Co. Limerick (Ní Chatháin 2002). The R. Deel had typically between 19 and 44 species per diatom sample analyzed.  The difference may have been due to the unusual weather conditions of summer 2002. Above average rainfall in June and July gave rise to flood conditions in rivers in early summer 2002, which may have had a short-term negative impact on diatom diversity.

In this study, only 40 species (56.3%) reached an abundance of greater than or equal to 1% abundance in the river samples. Only 22 species (31%) were identified from ten or more rivers investigated, and only 16 species (22.5%) were identified from 15 or more rivers investigated. This has also been found in other studies e.g. in Britain, for example Kelly et al. (1995) in a comparative study on diatom indices found that of the 150 species found in the 70 samples of the study, only 26 species were found in ten or more samples, and only thirteen species in 30 or more samples.

The actual number of species identified in this study (71 species) is lower than the number (103) identified from the R. Deel, Co. Limerick (Ní Chatháin, 2002). The difference, which is quite substantial, is likely due to repeated multi-seasonal sampling in the R. Deel study. Rott et al. (1998) identified 138 species from the Grand River, Ontario over a five-month period. Moore (1976) identified 93 diatom species from the R. Avon in southern England; Moore (1977) identified 117 diatom species in a eutrophic tributary of the R. Wylye in southern England; Cox (1990) identified over 150 species from a small softwater stream in West Germany; and Sabater and Sabater (1988) identified 125 species from the R. Ter in Spain. Again, these were all long-term studies as opposed to the once-off sampling involved in the investigation of lowland rivers in this project.

The majority of the species identified are components of the epilithon, however some are common on silt covered stones, particularly in lowland streams (e.g. Navicula tripunctata and Navicula lanceolata), and some are epiphytic species common on Cladophora glomerata filaments (e.g. Cocconeis placentula and Rhoicosphenia abbreviata). The common species in the dataset have also commonly been found in other studies of epilithic diatoms in Ireland, Europe and Canada (e.g. Ní Chatháin 2002, Kelly and Whitton 1995, Rott et. al. 1998, Sabater et al. 1987, Sabater et al. 1988). The species Achnanthes minutissima in particular is present in the majority of epilithic diatom river studies in Ireland, Britain, Europe, Canada and the US (Ní Chatháin 2002, Sabater et. al. 1988, Tomas and Sabater 1985, Cox 1990, Dixit and Smol 1994, Pan et al. 1996, and Rott et al. 1998). This species has a widespread distribution in circumneutral rivers and can be found growing attached to rocks and plants, particularly in fast flowing well aerated streams (Kelly, 2000).

Another common species identified is Amphora pediculus and this species is found on various substrates in streams, including rocks, sand, and attached to other algae. A. pediculus tends to like eutrophic rivers free from significant organic pollution where it is found alongside species such as Diatoma vulgaris (Fig. 4n), Navicula tripunctata and Nitzschia dissipata. It is an alkaliphilous species and prefers eutrophic to mesotrophic conditions (Telford, 2002). Cocconeis placentula was another common and often abundant component of the diatom flora from the lowland rivers investigated. This species is a well-known epiphtye (grows attached to plants) of green alga Cladophora glomerata in rivers but is also found growing abundantly on rocks. It is an abundant species across a wide range of chemical conditions (Kelly, 2000), and is also alkaliphilous and prefers eutrophic to mesotrophic conditions (Telford, 2002).

Other common, and often abundant species in this study included Navicula cryptotenella, Gomphonema minutum, Navicula lanceolata, Navicula tripunctata, and Rhoicosphenia abbreviata. Navicula cryptotenella, although strictly part of the silt flora, is also common on rocks in lowland rivers, particularly in hard water areas (Kelly, 2000). Navicula lanceolata and Navicula tripunctata, commonly found as part of the silt flora, are common species on rocks particularly in lowland streams across a wide range of water qualities (Kelly, 2000). Rhoicosphenia abbreviata is found primarily as an epiphyte on submerged plants, particularly Cladophora glomerata and has a very wide distribution.

References

Allott, T.E.H. and Flower, R.J. 1997. Epilithic diatoms in Welsh lakes and streams. ECRC Research Report, No. 35. Ensis, London.

CEN 13946, 2000. Water quality - Guidance standard for the routine sampling and pretreatment of benthic diatoms from rivers. CEN/TC 230 – European Committee for Standardization.

Cox, E.J. 1990 Studies on the algae of a small softwater stream I. Occurrence and distribution with particular reference to the diatoms. Archiv für Hydrobiologie 4, 525-552.

Dalton, C. 2000 Organic acidity in lake waters in Connemara, western Ireland: A preliminary investigation using diatom analysis. Verh. Internat. Verein. Limnol 27, 1193-1198.

Dixit, S.S. and Smol, J.P. 1994 Diatoms as indicators in the environmental monitoring and assessment program-surface waters (EMAP-SW). Environmental Monitoring and Assessment 31, 275-306.

Goldsmith, B.J. 2000 A diatom-based model to monitor trophic status in lowland rivers using artificial substrata. Ph.D. thesis. University College London.

Graham, L.E. and Wilcox, L.W. 2000 Algae. Prentice Hall, Upper Saddle River, NJ.

Kelly, M.G. and Whitton, B.A. 1995 The Trophic Diatom Index: a new index for monitoring eutrophication in rivers. Journal of Applied Phycology 7, 433-444.

Kelly, M.G. 2000 Identification of Common Benthic Diatoms in Rivers – a publication for the use of participants at the ‘Algal Training Course’.  University of Durham, UK.

Kelly, M.G., Adams, C., Graves, A.C., Jamieson, J., Krokowski, J., Lycett, E.B., Murray-Bligh, J., Pritchard, S. and Wilkins, C. 2001 The Trophic Diatom Index: A user’s manual. R & D Technical Report E2/TR2.

Kent, M. and Coker, P. 1994 Vegetation description and analysis: A practical approach. Belhaven Press, London.

Krammer, K. and Lange-Bertalot, H. 1986 Süsswasserflora von Mitteleuropa. Bacillariophyceae 2/1 Naviculaceae. Gustav Fischer, Stuttgart.

Krammer, K. and Lange-Bertalot, H. 1988 Süsswasserflora von Mitteleuropa. Bacillariophyceae 2/2 Epithemiaceae, Surirellaceae. Gustav Fischer, Stuttgart.

Krammer, K. and Lange-Bertalot, H. 1991a Süsswasserflora von Mitteleuropa. Bacillariophyceae 2/3 Centrales, Fragilariaceae, Eunotiaceae. Gustav Fischer, Stuttgart.

Krammer, K. and Lange-Bertalot, H. 1991b Süsswasserflora von Mitteleuropa. Bacillariophyceae 2/4 Achnanthaceae und Gomphonema. Gustav Fischer, Stuttgart.

Lucey, J., Bowman, J.J., Clabby, K.J., Cunningham, P., Lehane, M., MacCárthaigh, M., McGarrigle, M.L. and Toner P.F. 1999 Water quality in Ireland 1995-1997. Environmental Protection Agency, Ireland.

Ní Chatháin, B. 2002 Investigation of the ecology of benthic algae in the river Deel, South-West Ireland. Ph.D. thesis. University of Limerick.

Pan, Y., Stevenson, R.J., Hill, B.H., Herlihy, A.T. and Collins, G.B. 1996 Using diatoms as indicators of ecological conditions in lotic systems: a regional assessment. J. N. Am. Benthol. Soc. 15 (4), 481-495.

Prygiel, J., Whitton, B.A. and Bukowska, J. (eds.) 1999 Use of Algae for MonitoringRrivers III. Agence de l’Eau Artois-Picardie, Douai, France.

Moore, J.W. 1976 Seasonal succession of algae in rivers. I. Examples from the Avon, a large slow-flowing river. Journal of  Phycology 12, 342-349.

Moore, J.W. 1977 Seasonal succession of algae in a eutrophic stream in southern England. Hydrobiologia. 53(2), 181-192.

Norton, T.A., Melkonian, M. and Andersen, R.A. 1996 Algal biodiversity. Phycologia 35, 308-326.

Rott, E., Duthie, H.C., and Pipp, E. 1998 Monitoring organic pollution and eutrophication in the Grand River, Ontario, by means of diatoms. Can. J. Fish. Aquat. Sci. 55, 1443-1453.

Round, F.E., Crawford, R.M. and Mann, D.G. 1990 The Diatoms – Biology and morphology of the genera. Cambridge University Press, Cambridge, UK.

Round, F.E. 1993 A review and methods for the use of epilithic diatoms for detecting and monitoring changes in river water quality. Methods for the examination of water and associated materials. HMSO, London.

Sabater, S., Sabater, F. and Tomas, X. 1987 Water quality and diatom communities in two Catalan rivers (N.E. Spain). Water Research 21, 901-911.

Sabater, S. and Sabater, F. 1988 Diatom assemblages in the River Ter. Arch. Hydrobiol. 111(3), 397-408.

Sabater, S., Sabater, F. and Armengol, J. 1988 Relationships between diatom assemblages and physico-chemical variables in the River Ter (NE Spain). Int. Revue ges. Hydrobiol. 73 (2), 171-179.

Telford, R. Down loaded on the 31/10/2002

http://www.staff.ncl.ac.uk/r.j.telford/diatoms/index.htm

Tomas, X. and Sabater, S. 1985 The diatom associations in the Llobregat river and their relations to water quality. Verh. Int. Verein. Limnol. 22, 2348-2352.

Van Dam, H. 1982 On the use of measures of structure and diversity in applied diatom ecology. Nova Hedwigia 73, 97-115.

WFD. 2000 Water Framework Directive. Council of the European Union: Directive 2000/60/EC of the European parliament and of the Council of 23 October 2000 establishing a framework for Community action in the field of water policy. Official Journal of the European communities. L/327 43, 72 pp.

Whitton, B.A., Rott, E. and Friedrich, G. (eds.) 1991 Use of algae for monitoring rivers. Institut für Botanik, Univ. Innsbruck, Innsbruck, Austria.

Whitton, B.A. and Rott, E. (eds.) 1996 Use of algae for monitoring rivers II. Institut für Botanik, Univ. Innsbruck, Innsbruck, Austria.

# Text boxes

Fig. 1. Scatterplot of diatom occurrence and maximum abundance for the 25 lowland Irish rivers sampled.

A.l. – Achnanthes lanceolata

Cyc.men. – Cyclotella meneghiana

C.m. – Cymbella minuta

C.s. – Cymbella sileascia

D.v. – Diatoma vulgaris

F.c. – Fragilaria capucina

F.v. – Fragilaria capucina var. vaucherie

G.a. – Gomphonema angustum

G.o. – Gomphonema olivaceum

G.p. – Gomphonema parvulum

N.cep. – Navicula cryptocephala

N.c. – Navicula cryptotenella

N.g. – Navicula gregaria

N.m. – Navicula menisculus

N.r. – Nitzschia recta

N.t. – Navicula tripunctata

R.a. – Rhoicosphenia abbreviata

S.u. – Synedra ulna

N.cep.

N.m.

N.r.

Melosira varians

G.a

Cyc. men

C.s.

F.c.

Reimeria sinuata

D.v.

Nitzschia palea

G.p.

N.g.

Nitzschia dissipata

A.l.

Cocconeis pediculus

Caloneis bacillum

F.v.

G.o.

C.m.

S.u.

N.t., R.a.

Navicula lanceolata

Gomphonema minutum

N.c.

Cocconeis placentula

Amphora pediculus

Achnanthes minutissima

Number of occurrences

Maximum abundance (%)

75

50

25

0

25

20

15

10

5

0

Fig. 2. DCA plot for 24 rivers sampled. (Cannahowna river not included.)

Tar

Arra

Little Brosna

Maigue

Mulkear

Dead

Kilcolgan

Kilmastulla

Nore

Dinin

Erkina

Deel

Suir

Gweestion

Aherlow

Kings

Nenagh

Anner

Silver

Sinking

Clare

Boyne Upper

Camlin

Multeen

+4.5

+0.0

+4.0

+0.0

Fig. 3. DCA plot for the 71 species identified from 24 lowland Irish rivers (no data for the Cannahowna river). For names of species refer to Table 2.

22

38

27

46

52

57

47

66

65

56

44

23

42

35

54

15

18

39

64

48

4

59

30

3

43

70

16

60

12

29

34

7

41

5

53

49

21

31

10

17

69

1

11

26

67

24

62

51

58

13

61

25

28

32

33

36

2

19

55

9

20

8

40

37

68

71

6

14

63

50

+4.5

+0.0

+4.0

+0.0

Fig. 4. a- Fragilaria construens; b- Cocconeis placentula; c-Cocconeis pediculus; d-Cocconeis placentula; e-Synedra ulna; f -Caloneis bacillum; g-Amphora inariensis; h Stauroneis phoenicenteron; i-Navicula reinhardti; j-Cymbella sp.; k-Achnanthes minutissima; l-Cymbella minuta; m Gomphonema sp.; n-Diatoma vulgaris; o Cyclotella meneghiana.

o

m

n

i

j

k

l

b

c

e

d

f

g

h

a